## Slide 1
Optimizing Interconnection Complexity for
Realizing Fixed Permutation in Data and Signal Processing Algorithms
Ren Chen, Viktor K. Prasanna
Ming Hsieh Department of Electrical Engineering
Presented by:
Ajitesh Srivastava, Department of Computer Science
University of Southern California
Ganges.usc.edu/wiki/TAPAS

## Slide 2
Introduction
Background and Related Work
High Throughput and Energy Efficient Design
Experimental Results
Conclusion and Future Work
Outline
Notes: I’ve divided my talk into six parts.
First I’ll introduce the permutation on streaming data and problem definition.
Then I’ll discuss on the existed state-of-the-art solutions for permutation in hardware.
Later I’ll present our proposed novel mapping approach and the details of the algorithm.
Finally I’ll demonstrate our experimental results
and make conclusions on our work

## Slide 3
Permutation
  A permutation can be represented using
  is the size of vectors and
  The bit matrix is called as a permutation matrix
Permutation
Sorting network
FFT network
Notes: A permutation can be presented using matrix, the permutation matrix denoted as Pm determines the permutation pattern.

## Slide 4
Key Algorithms: FFT, sorting, Viterbi decoding, etc.
Related Applications
Frequency domain
in images
Image filtering
Audio analysis
Bitonic sort
Partial differential equations
OFDM System
Notes: Data permutations widely exist in data or signal processing algorithms, such as FFT, bitonic sorting, viterbi decoding, etc.
And these algorithms are kernels of various applications.

## Slide 5
Data Permutation in Conventional Architectures
Permutation by wires
  Parallel architecture
Permutation by memory
or registers
  Pipeline architecture
  Shared memory architecture
Notes: Data permutations can be realized using memory, registers, or wires
parallel architecture shown in the figure b) uses wires to do data permutation.
Pipeline architecture and shared memory use memory or registers to do data permutation.
For example, the delay feedback or commutator in the hardware implementation of FFT

## Slide 6
Data Permutation in Streaming Architectures
Streaming architecture
  High data parallelism
  High design throughput
  Simple control scheme
  No requirement on data input/ output order
Notes: Streaming architectures are popular for hardware implementation of data or signal processing algorithms,
due to their higher data parallelism, higher throughput, and simple control scheme.
The key issue for implementing streaming architecture is how to realize permutation on streaming data.
The figure below shows how data sequences are permuted by streaming permutation:
Some data sequences are flowing into the stream permutation block, 4 inputs per clock cycles,
after a certain delay, the permuted data sequences flow out of the block, and also 4 outputs per clock cycle.
(Not required to explain)
With continuous input of data streams, the throughput of this design is 4 data results per clock cycles.
Assuming the data width per output is 32-bit, the clock period is 4 ns, then the throughput is 32 Gb/s.

## Slide 7
Permute streaming data with a fixed data parallelism
Input/output: in a streaming manner and at a fixed rate
Data parallelism : # of inputs processed each cycle per computation stage
Streaming permutation: permutation between adjacent computation stages
Processing elements: computation units for a given application
Problem Definition
Notes: In summary, the problem to be solved in this paper is to permute streaming data with a fixed data parallelism.
We have streaming data input and output.
Each cycle p data inputs and outputs.
Data permutations are performed between adjacent computation stages.
Fig. shows the architectural framework within which we propose our data permutation approach using FPGA as the target platform.

## Slide 8
Introduction
Background and Related Work
High Throughput and Energy Efficient Design
Experimental Results
Conclusion and Future Work
Outline

## Slide 9
Related Work (JVSP ’07, T. JARVINEN)
For stride permutation on
array processor
Flexible data parallelism
Mathematical formulation
Notes: There have been work proposed to realize permutation on streaming data, however mostly focused on specific permutation patterns, such as stride permutation in FFT.
In this related work, the author developed a streaming architecture for realizing stride permutation on array processor.

## Slide 10
Related Work (DAC ’12, M. Zuluaga and M. Püschel)
Domain-specific language based
Hardware generator for data permutations in sorting
Notes: In [28], the SPIRAL project develop
DSL (Domain Specific Language) to enable mapping sorting algorithms with
flexible design choices.
They developed a design automation tool to generate datapath for streaming permutation,
However their approach is expensive in both memory and control logic.

## Slide 11
Proposed Design Approach
Drawbacks of the state-of-the-art
  Only supports specific permutation patterns
  Design scalability needs to be improved
  Interconnection complexity is not considered
We propose a mapping approach to obtain a streaming permutation architecture
  Utilizes Benes network for building datapath and generating control logic
  Highly optimized wrt. memory efficiency and interconnection complexity
  Scalable with problem size and data parallelism
  Supports processing continuous data streams
  Design automation tool
Notes: For the existed state-of-the-art designs, some of them only supports specific permutation patterns,
Some of them are not memory or resource efficient.
In our work, we propose a novel mapping approach to obtain a streaming permutation architecture,
By utilizing Benes network to build the datapath and generating control logic
Our design proves to be highly optimized with regards to memory efficiency and interconnection complexity,
And highly scalable with problem size and data parallelism.
We also developed a design automation tool

## Slide 12
Introduction
Background and Related Work
High Throughput and Energy Efficient Design
Experimental Results
Conclusion and Future Work
Outline
Notes: Let’s continue to our proposed design approach

## Slide 13
Benes Network
Multistage network to realize all permutations
Rearrangeably non-blocking
Notes: I’d like to talk about Benes network before introducing our design approach.
Assuming n inputs and n outputs, Bene network is a multistage network to realize all n! permutations.
Rearrangeably non-blocking means that, we can always find a way to realize any fixed permutation by configuring the switches in the Benes network.
The figure on the right shows the 8-input Benes network

## Slide 14
Parameterized architecture
  Problem size
  Data parallelism
Memory based
  independent memory blocks
  Each of size
-to- connection network
  switches
  Optimal compared with state
  -of-the art
Highly optimized control unit
Architecture Overview
Notes: Fig. on the right shows the overall architecture of the streaming design.
Design parameters include problem size N and data parallelism p.
The datapath consists of two p-to-p connection networks, one memory array including p independent memory blocks, each of size N=p.
The control unit has two configuration tables to reconfigure the connection networks dynamically, and one address generation unit (AGU) for memory access.
Each connection network has log p stages of 2x2 switches. Each stage has p=2 switches. Thus, a connection network utilizes (p=2) log p 2x2 switches,
which is asymptotically optimal compared with state-of-the-art [1, 8, 6].
(No need to explain only if asked:)
We consider using two different memory architectures: each memory has one read port and one write port, or each memory has a concurrent read-before-write port
(two data ports sharing one address port).

## Slide 15
Generating the Datapath (1)
Generating Datapath
  : input size
  : data parallelism
  , : 2x2 switch
  : subnetwork of size
  , : -input block
  , : 2x2 switch
  : -to- wire connection
Notes: The right figure shows the key idea of generating the datapath of our design uisng Benes network
We propose a divide-and-conquer based mapping approach.
As shown in the right figure, the Benes network has been decomposed into p subnetworks with log p stages of 2x2 switches on the left or right.
Correspondingly, p memory blocks in our proposed streaming permutation network are employed to realize the permutation of the p subnetworks temporally.
The SPN also has logp/2 stages of 2x2 switches on the left and right.
Explain the meaning of the notations if needed.
each of size〖 𝑆〗_2, where 𝑆_2 ≥𝑆_1 and N=𝑆_2×𝑆_1.

## Slide 16
Generating the Datapath (2)
For a fixed data parallelism , the streaming permutation network is able to realize arbitrary permutation
  In , =
  Permutation in is performed by temporally
  In , =
Number of switches:
Maximum wire length:
Notes: We theoretically prove that for a fixed data parallelism , the streaming permutation network is able to realize arbitrary permutation with the listed three assumptions.
And based on our data path generation algorithm, the total number of 2x2 switches is plogp,
The maximum wire length is o(p), the number of n/p-entry memory is p.
each of size〖 𝑆〗_2, where 𝑆_2 ≥𝑆_1 and N=𝑆_2×𝑆_1.

## Slide 17
Optimization of Interconnection Complexity (1)
Configuration bits of switch in different states
  input of Benes network, output of Benes network
  configuration bits for , : configuration bit for
  Two states for a switch: pass or cross
Notes: Let’s continue with our algorithm for generating the control logic.
The key idea is to configure the Benes network for a given fixed permutation. The resulting configuration bits are then taken as input to generate the configuration
tables and the AGU shown in the figure in slides 14.
A 2 x 2 switch of a Benes network will be either in pass state or cross state, which can be represented by a Boolean variable.
As shown in the figure, let X and Y be the set of inputs and outputs of a Benes network respectively,
let a : X -> {0, 1} and b : Y -> {0, 1}, where a(i) is the configuration bit of X(i), and b(i) is the configuration bit of Y (i).
(No need to explain only if needed)
Explain:
For input switch
a0=0, means input 0 will be routed to the upper side, a1=1, means input 1 will be routed to the lower side.
a3=0, means input 3 will be routed to the upper side, a2=1, means input 2 will be routed to the lower side.
similarly for output switch
each of size〖 𝑆〗_2, where 𝑆_2 ≥𝑆_1 and N=𝑆_2×𝑆_1.

## Slide 18
Optimization of Interconnection Complexity (2)
Key Idea
  A null switch can be replaced by wires
  A null switch: always in either pass or cross state
Notes: We define a null switch as a switch which is always in either pass or cross state.
The key idea to optimize the interconnection complexity is to replace the null switches with wires.
As shown in the right figures, the null switches in the top right figure are replaced with wires in the bottom right figure, as these switches are constantly in either pass or cross state.
each of size〖 𝑆〗_2, where 𝑆_2 ≥𝑆_1 and N=𝑆_2×𝑆_1.

## Slide 19
Optimization of Interconnection Complexity (3)
End-to-End Routing
  Called for computing
  configuration bits
  : input data vector
  : permuted data vector
  : mapping from to
  : output data vector of
  input switches
  y: input data vector of
  output switches
Notes: The EER procedure returns four vectors including a, b, x’, y’
a and b are the configuration bits for data vector x and y,
After a and b are determined, x is the input of input switches, and x’ is the resulting data vector;
y is the output of output switches, and y’ is the input of the output switches.
Each time when calling EER (end-to-end routing), the algorithm will search for solutions to configure the input and output switch,
i.e., to determine the value of a and b.
After the values of a and b are determined, the x will be routed by the input switch to obtain x’, and the y will be routed by the output switch to obtain y’
As limited by time, I will bypass the details of our EER algorithm, for more details please refer our paper.
each of size〖 𝑆〗_2, where 𝑆_2 ≥𝑆_1 and N=𝑆_2×𝑆_1.

## Slide 20
Optimization of Interconnection Complexity (4)
Heuristic Routing Algorithm:
RT procedure
  Compute the configuration
  bits of and in steps
  Results vary in different runs
  Iteratively called many times
Notes: We propose a heuristic routing algorithm to maximize the number of null switches in the proposed streaming permutation network
The algorithm will call RT procedure several times to compute the configuration bits of LB and RB in log p steps.
As shown in the right figure, RT takes as inputs parameters including x, y, and p.
When p > 1,
RT() will be called to route the upper subnetwork and the lower subnetwork.
Otherwise,
ai, bi, Xi and Yi obtained by EER will be returned.
As limited by time, I will bypass the details of our RT algorithm, for more details please refer our paper.
each of size〖 𝑆〗_2, where 𝑆_2 ≥𝑆_1 and N=𝑆_2×𝑆_1.

## Slide 21
Optimization of Interconnection Complexity (5)
Heuristic Routing Algorithm
  Call RT procedure to compute
  configuration bits
  Search for the solution having
  maximum number of null switches
Notes: By iteratively call the RT procedure, our proposed heuristic routing algorithm will search for the solution having the maximum number of null switches.
The algorithm will be run statically with a time complexity of O(n2log p) to generate the datapath of the proposed streaming permutation network.
each of size〖 𝑆〗_2, where 𝑆_2 ≥𝑆_1 and N=𝑆_2×𝑆_1.

## Slide 22
Resource Consumption Summary
Designs in [1] and [8]
  Only support specific family of permutation
  Our design consumes same amount of resource in the worst case
Design in [9]
  Our design uses half amount of memory
  Both consume logic for mux
Notes: Please just summarize as the texts in the slides

## Slide 23
Introduction
Background and Related Work
High Throughput and Energy Efficient Design
Experimental Results
Conclusion and Future Work
Outline

## Slide 24
Throughput
  Defined as the number of bits permuted per second (Gbits/s)
  Product of number of data elements permuted per second and data width per element
Energy efficiency
  Defined as the number of bits permuted per unit energy consumption (Gbits/Joule)
  Calculated as the throughput divided by the average power consumption
Performance metrics

## Slide 25
Platform and tools
  Xilinx Virtex-7 XC7VX980T , speed grade -2L
  Xilinx Vivado 2015.2 and Vivado Power Analyzer
Input vectors for simulation randomly generated
Performance metrics
  Resource consumption
  Throughput
  Energy efficiency
Experimental Setup
Notes:     Just repeat the content in this slides
    Note to say:
    As the cost of our design datapath does not depend on the specific
    permutation to be performed, we choose one randomly for
    various N and p in experiments. The same permutations are
    also chosen for our baselines.

## Slide 26
BRAM consumption of the proposed design
  [9] uses BRAM-LUT mostly for realizing the 2p memory blocks
  Our design consumes the same amount of BRAMs (O(p)) compared with [8]
  Note designs in [8] only realize bit index permutations
Experimental Results (1)
Notes: Each BRAM18 has 18kb, if the memory requirement is < 18kb, then a BRAM18 will be used.
If the memory requirement is between 18 kb and 36 kb, then two BRAM18 will be used.
In the left figure,
our design and design in [8] need p memory blocks, each of size N/p (ours), and 2N/p ([1]) .
When p changes, N/p and 2N/p are always < 18kb, so the number of BRAMs are the same.
Design in [9] needs 2p memory blocks, each of size 2N/p, however, it only uses distributed RAM to replace BRAM for different memory size.
In the right figure, when p > 32, our design and design in [8] consume the same amount of BRAMs. (Similar explanation can be explained)
In the second stage of SPN, memory power consumption issue
Solution: data remapping technique
  Use single-port memory blocks in stage 1 of the permutation block
  Use the same address for memory read and write
  Logic to update the memory access address in each cycle
Data Remapping:
  Permutation matrix 𝑃 to represent permutation in time
  For 𝑖th permutation, in cycle 𝑗, 𝐴_(𝑖−1)[𝑗] is the address
  There always exist a constant 𝑞 such that 𝑃^(𝑞+1)=𝐼,
  and 𝐴_𝑞×𝑃=〖𝐴_(𝑞−1)×𝑃〗^2=…=〖𝐴_0×𝑃〗^(𝑞+1)=𝐴_0
  Theorem 4:
For streaming stride permutation, a constant number
of address sequences need to be generated

## Slide 27
LUT consumption of the proposed design (for various )
  22.1%~65.7% less LUTs compared with [8]
  59.1%~96.4% less LUTs compared with [9]
Experimental Results (2)
Notes: This slides show the LUT consumption of our design and the baselines
Compared to the design in [8], our design reduces the LUT consumption by 22.1%~65.7% benefiting from our mapping approach.
As the design in [9] uses distributed RAM for memory implementation, our design uses 59.1%~96.4% less LUTs compared with [9]
In the second stage of SPN, memory power consumption issue
Solution: data remapping technique
  Use single-port memory blocks in stage 1 of the permutation block
  Use the same address for memory read and write
  Logic to update the memory access address in each cycle
Data Remapping:
  Permutation matrix 𝑃 to represent permutation in time
  For 𝑖th permutation, in cycle 𝑗, 𝐴_(𝑖−1)[𝑗] is the address
  There always exist a constant 𝑞 such that 𝑃^(𝑞+1)=𝐼,
  and 𝐴_𝑞×𝑃=〖𝐴_(𝑞−1)×𝑃〗^2=…=〖𝐴_0×𝑃〗^(𝑞+1)=𝐴_0
  Theorem 4:
For streaming stride permutation, a constant number
of address sequences need to be generated

## Slide 28
LUT consumption of the proposed design (for various )
  27.3%~75.8% less LUTs compared with [8]
  42.2%~92.3% less LUTs compared with [9]
Experimental Results (3)
Notes: This slides show the LUT consumption of our design and the baselines for various N
Compared to the design in [8], our design reduces the LUT consumption by 27.3%~75.8% benefiting from our mapping approach.
As the design in [9] uses distributed RAM for memory implementation, our design uses 42.2%~92.3% less LUTs compared with [9]
In the second stage of SPN, memory power consumption issue
Solution: data remapping technique
  Use single-port memory blocks in stage 1 of the permutation block
  Use the same address for memory read and write
  Logic to update the memory access address in each cycle
Data Remapping:
  Permutation matrix 𝑃 to represent permutation in time
  For 𝑖th permutation, in cycle 𝑗, 𝐴_(𝑖−1)[𝑗] is the address
  There always exist a constant 𝑞 such that 𝑃^(𝑞+1)=𝐼,
  and 𝐴_𝑞×𝑃=〖𝐴_(𝑞−1)×𝑃〗^2=…=〖𝐴_0×𝑃〗^(𝑞+1)=𝐴_0
  Theorem 4:
For streaming stride permutation, a constant number
of address sequences need to be generated

## Slide 29
Throughput performance of the proposed design
  Our designs achieve
    Up to 73.2% throughput improvement compared with [8]
  Up to 129% throughput improvement compare with [9]
Experimental Results (5)
Notes: We assume the design throughput is only determined by the data parallelism and the maximum operating frequency reported by the post place-and-route results.
The left Fig. demonstrates the design throughput for various N with p = 4.
As the problem size increases, the throughput decreases due to the lower achievable maximum operating frequency by the design.
As shown in the figure, our design is able to sustain 71%~80% of the DDR3 peak bandwidth, (approximately 10 GBytes/s [13]) for various N with p = 4.
We employed a balanced pipelining approach for the purpose of trade off between energy efficiency and throughput.
Left Fig. shows that compared with the baselines, the throughput is improved significantly (up to 73.2%) in our design, especially for large problem sizes. Such performance
improvement can be expected considering that less BRAM blocks and LUTs are used in our design.
Right fig. demonstrates the design throughput for various p with N = 8192.
This Fig. also shows that the DDR3 peak bandwidth can be easily saturated when p > 16. In such cases, we can only employ the on-chip BRAMs with
extremely high bandwidth as the data memory. This also implies that a potential high memory bandwidth utilization may be achieved if using the emerging 3D stacked memory providing up to 16x more throughput than DDR3 [13].
In the second stage of SPN, memory power consumption issue
Solution: data remapping technique
  Use single-port memory blocks in stage 1 of the permutation block
  Use the same address for memory read and write
  Logic to update the memory access address in each cycle
Data Remapping:
  Permutation matrix 𝑃 to represent permutation in time
  For 𝑖th permutation, in cycle 𝑗, 𝐴_(𝑖−1)[𝑗] is the address
  There always exist a constant 𝑞 such that 𝑃^(𝑞+1)=𝐼,
  and 𝐴_𝑞×𝑃=〖𝐴_(𝑞−1)×𝑃〗^2=…=〖𝐴_0×𝑃〗^(𝑞+1)=𝐴_0
  Theorem 4:
For streaming stride permutation, a constant number
of address sequences need to be generated

## Slide 30
Energy efficiency comparison
  2.1x~3.5x energy efficiency improvement compared with the state-of-the-art in [9]
  1.2x~1.5x energy efficiency improvement compared with the state-of-the-art in [8]
Experimental Results (6)
Notes: We also evaluate the energy efficiency of our design. We only focus on the dynamic power consumption of our proposed permutation
design and the baselines. The left figure demonstrates the energy efficiency for various N from 128 to 8192
with p = 4. It can be observed that the energy efficiency drops significantly when N = 2048. This is due to the
fact that the number of BRAMs used starts to increase with N when N > 2048. The result also shows that as the
problem size is varied, our design achieves 2.1x~3.5x improvement in energy efficiency compared with design in [8].
The right figure demonstrates the energy efficiency when varying p
with N = 8192. As noted in figure in slides 31, the LUT consumption dramatically increases with p,
the energy efficiency decreases significantly accordingly. As shown in the right figure, for
various p, our design improves energy efficiency by up to 3.5x compared with the baselines
In the second stage of SPN, memory power consumption issue
Solution: data remapping technique
  Use single-port memory blocks in stage 1 of the permutation block
  Use the same address for memory read and write
  Logic to update the memory access address in each cycle
Data Remapping:
  Permutation matrix 𝑃 to represent permutation in time
  For 𝑖th permutation, in cycle 𝑗, 𝐴_(𝑖−1)[𝑗] is the address
  There always exist a constant 𝑞 such that 𝑃^(𝑞+1)=𝐼,
  and 𝐴_𝑞×𝑃=〖𝐴_(𝑞−1)×𝑃〗^2=…=〖𝐴_0×𝑃〗^(𝑞+1)=𝐴_0
  Theorem 4:
For streaming stride permutation, a constant number
of address sequences need to be generated

## Slide 31
Conclusion and Future Work
31
Conclusion
  Streaming data permutation architecture
    Scalable with data parallelism and problem size
    Efficient data permutation realization
    Highly optimized with interconnection complexity
    High throughput and resource efficient
Future work
  Automatic generation of high throughput resource efficient signal and data processing kernels

## Slide 32
32
Thanks!
Questions?
Ganges.usc.edu/wiki/TAPAS