## Slide 1: DT-CGRA: Dual-Track Coarse-Grained Reconfigurable Architecture for Stream Applications
Xitian Fan, Huimin Li, Wei Cao, Lingli Wang
Fudan University

## Slide 2
Outline
The dual-track programming model
The dual-track CGRA architecture
Computing pattern examples
Experiments
Summary

## Slide 3
Outline
The dual-track programming model
The dual-track CGRA architecture
Computing pattern examples
Experiments
Summary

## Slide 4
Observations from object detection/classification domain:
Deep learning : CNN
The Dual-Track Programming Model (1)
convolution
…
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
pooling
…
…
…
fully connected
…
duplicate of input data

## Slide 5
Observations from object detection/classification domain:
Deep learning : CNN
The Dual-Track Programming Model (1)
Kernel function | Kernel Scope
Convolution | 
Pooling | 
Matrix multiplication | 
Kernel function | Kernel Scope
Convolution | 
Pooling | 
Matrix multiplication | 
Computing abstraction:
A kernel function do computation over a limited kernel scope.
The kernel scope shifts in a specific order with a stride.

## Slide 6
What is the dual-track programming model ?
The kernel functionality remains unchanged.
The data in the kernel scope have changed.
From the hardware perspective:
Computing components are configured only once.
Data managers are required to control data streams.
Pseudo-static configuration
load
store
Computing Components
Dynamic configuration
DMAs
The Dual-Track Programming Model (2)
Need reconfiguration when kernel function is changed

## Slide 7
pseudo-static configuration
load
store
Computing Components
dynamic configuration
DMAs
Determine the functionality of computing components
Determine the behavior of DMAs
What is the dual-track programming model ?
dual-track
The Dual-Track Programming Model (3)

## Slide 8
Outline
The dual-track programming model
The dual-track CGRA architecture
Computing pattern examples
Experiments
Summary

## Slide 9
The Dual-Track CGRA (1)
Interconnection between multi-channel data bus and RCs
Interconnection among RCs
Off-chip memory DMA interface
Interface with other node
Dynamic configuration interface
Pseudo-static configuration interface
CA | Computing Array
Pseudo-static configuration
load
store
Computing Components
Dynamic configuration
DMAs
SBU | Stream Buffer Unit
RC | Reconfigurable Cell
PRC | Reconfigurable Cell to calculate Power function
IRC | Reconfigurable Cell to calculate Interpolation

## Slide 10
The Dual-Track CGRA (2)
RC unit
SRAM
SRAM
SRAM
FIFO
FIFO
FIFO
Ctr Unit
FIFO
FIFO
“map” part
“reduce” part
FIFO | 
SRAM | 
Multiplier | 16 bit
ALU | 16 bit
Simplify the control flow.
Reduce the bandwidth of the output interface.
Support configuration, decomposition and combination.

## Slide 11
The Dual-Track CGRA (3)
SRAM
SRAM
SRAM
FIFO
FIFO
FIFO
Ctr Unit
FIFO
FIFO
“map” part
“reduce” part
Computing pattern examples:
1
RC unit

## Slide 12
The Dual-Track CGRA (4)
SRAM
SRAM
SRAM
FIFO
FIFO
FIFO
Ctr Unit
FIFO
FIFO
“map” part
“reduce” part
Computing pattern examples:
2
RC unit

## Slide 13
Suppose: a kernel requires 5 multiplier-adders
The Dual-Track CGRA (5)
RC unit

## Slide 14
The Dual-Track CGRA (6)
PRC & IRC unit
PRC : special RC to calculate based on fast inverse square root algorithms.
Example code to calculate :
float InvSqrt(float x)
{
float xhalf = 0.5f*x;
int i = *(int*)&x;
i = 0x5f3759df - (i>>1);
x = *(float*)&i;
x = x*(1.5f-xhalf*x*x);
return x;
}
IRC : interpolation for transcendental functions that can be approximated by piecewise function.
(a) PRC
(b) IRC

## Slide 15
The Dual-Track CGRA (7)
Interconnections among RCs: horizontal interconnections
…
…
RC
RC
RC
RC
RC
RC
RC
…
Elastic data transmission
Simplify the control behavior
RC
valid
stop
valid
stop

## Slide 16
The Dual-Track CGRA (8)
Interconnections among RCs: vertical interconnections
Input interface
Output interface
RC
RC
…
RC
RC
…
To next row of RC
…
Multi-Channel data bus
data
sel
valid
stop

## Slide 17
The Dual-Track CGRA (9)
Stream Buffer Unit: SBU
Stream Register File
DMA
WrBus
RdBus
ExternalBus
Double buffer technique to reduce configuration overhead
Controlled dynamically by VLIW
execution time
configure
configure
configure
execution
execution
idle state of configuration

## Slide 18
The Dual-Track CGRA (10)
Detail information of each unit in DT-CGRA
Unit type | Information | 
 | Details | Number
RC | 16 bit fixed-point | 
PRC | 16 bit fixed-pointa | 2
IRC | 16 bit fixed-point | 3
FIFO | , 128 Byte | RC: 5; PRC: 3; IRC: 2
SRAM | , 512 Byte | 3 for each RC
SBU | 1 SRF | 16
SRF | , 2 KByte | 16
Unit type | Information | 
 | Details | Number
RC | 16 bit fixed-point | 
PRC | 16 bit fixed-pointa | 2
IRC | 16 bit fixed-point | 3
FIFO |  | RC: 5; PRC: 3; IRC: 2
SRAM |  | 3 for each RC
SBU | 1 SRF | 16
SRF |  | 16

## Slide 19
Outline
The dual-track programming model
The dual-track CGRA architecture
Computing pattern examples
Experiments
Summary

## Slide 20
Computing Pattern Examples (1)
Convolution in CNN: one of the computing strategies
Kernel size: ; stride: 2.
…
…
…
…
…
…
Final convolution results
#Phase 0
convolution with the first row of R, G, B part of the kernel
#Phase 1
convolution with the second row of R, G, B part of the kernel
…
…
…
…

## Slide 21
Matrix multiplication: Fully connected Layer in CNN
FC6 in AlexNet:
is partitioned into smaller matrices
Batch processing.
Batch = 100
Computing Pattern Examples (3)

## Slide 22
Matrix multiplication: Fully connected Layer in CNN
for the -th SRAM:
storing with -th column of
SRAMs adopt double buffer technique to reduce the overhead of loading weights.
Computing Pattern Examples (4)

## Slide 23
Outline
The dual-track programming model
The dual-track CGRA architecture
Computing pattern examples
Experiments
Summary

## Slide 24
Experiments (1)
Implementation details
Synthesis | Synopsys Design Compiler
P & R | Synopsys IC Compiler
Power Estimation | IC Compiler
Process | SMIC 55 nm
Component | Area in | Power in
DT-CGRA architecture | 3,791,206.12 (100%) | 1786.20 (100%)
Combinational On-chip memory Registers Others | 705,199.20 (18.60%) 2,563,072.83 (67.61%) 409,032.48 (10.79%) 113,901.61 (3.00%) | 85.64 (4.79%) 960.43 (53.77%) 548.73 (30.72%) 191.40 (10.72%)
Component |  | 
DT-CGRA architecture | 3,791,206.12 (100%) | 1786.20 (100%)
Combinational On-chip memory Registers Others | 705,199.20 (18.60%) 2,563,072.83 (67.61%) 409,032.48 (10.79%) 113,901.61 (3.00%) | 85.64 (4.79%) 960.43 (53.77%) 548.73 (30.72%) 191.40 (10.72%)
Delay of critical path: 1.95ns;
1.79W @ 500MHz
78% in area
84% in power consumption

## Slide 25
Experiments (2)
Evaluation methods
A general flow of object detection/inference:
HOG
Feature extraction
Feature selection
Inference
CNN
k-means
SPM
PCA
SVM
Softmax
Joint Bayesian
Results: person, pedestrian

## Slide 26
Experiments (3)
Evaluation methods
Algorithm | Implementation | Scenario | Problem size
HOG | OpenCV 2.7.9 | Pedestrian Detection | each detection window:
CNN | Caffe | Alext-Net in object detection | Each patch:
k-means | OpenCV 2.7.9 | Object classification | Vocabulary size: 200
PCA | OpenCV 2.7.9 | Face detection | Input dimension:32000 Output dimension: 150
SPM | OpenCV 2.7.9 | Object Classification | Pyramid layer: 3 Vocabulary size: 200
Softmax | Caffe | Alex-Net in object detection | Class number: 1000
SVM | OpenCV 2.7.9 | Pedestrian Detection | Feature dimension: 3780
Joint Bayesian | OpenCV 2.7.9 | Face Detection | Feature dimension: 150
Algorithm | Implementation | Scenario | Problem size
HOG | OpenCV 2.7.9 | Pedestrian Detection | 
CNN | Caffe | Alext-Net in object detection | 
k-means | OpenCV 2.7.9 | Object classification | Vocabulary size: 200
PCA | OpenCV 2.7.9 | Face detection | Input dimension:32000 Output dimension: 150
SPM | OpenCV 2.7.9 | Object Classification | Pyramid layer: 3 Vocabulary size: 200
Softmax | Caffe | Alex-Net in object detection | Class number: 1000
SVM | OpenCV 2.7.9 | Pedestrian Detection | Feature dimension: 3780
Joint Bayesian | OpenCV 2.7.9 | Face Detection | Feature dimension: 150
CPU implementation:
Intel i7-3770 (3.4GHz)
Single thread
Power: 77 W

## Slide 27
Experiments (3)
CPU vs. DT-CGRA
Chart: CPU/Proposed Architecture
| HOG | CNN | k-means | PCA | SPM | Softmax | SVM | Joint-Bayesian
 | 5.1424 | 5.5364 | 63.7931 | 98.6979 | 27.9842 | 9.5833 | 89.5528 | 10.5911
Average speedup: 38.86x
(2) Energy consumption of CPU over the design architecture
(1) Speedup of the design architecture
Average energy reduction: 1442.7x
Chart: log(CPU/Proposed Architecture)
| HOG | CNN | k-means | PCA | SPM | Softmax | SVM | Joint-Bayesian
 | 2.2962 | 2.3106 | 3.3705 | 3.5604 | 3.0356 | 2.5483 | 3.5222 | 2.5923

## Slide 28
Experiments (4)
DT-CGRA vs. Application specific architectures
Solution on convNN | Time (ms) | Power (W) | Peak Peformance (GOP/s) | Energy-efficiency
ShiDianNao [18] | 0.047 | 0.32 | 194 | 6.90x
DT-CGRA | 0.058 | 1.79 | 95 | 1x
Solution on Alex-Net (five convolutional layers) | Time (ms) | Power (W) | Peak Peformance (GOP/s) | Energy-efficiency
FPGA2015 [19] | 21.61 | 18.61 | 61.62 | 1x
DT-CGRA | 28.72 | 1.79 | 95 | 7.82x
ShiDianNao [18]
convNN
1 GHz @ TSMC 65 nm process
4.86
16 bit
FPGA 2015 [19]
Five convolutional layers of AlexNet
100 MHz
Floating points.
DT-CGRA
500 MHz @ SIMC 55 nm process
16 bit
3.79
Roughly comparison results

## Slide 29
Summary
Propose a dual-track programming model for CGRA
Pseudo static configuration is to determine the functionalities of mapped RCs.
Dynamic configurations are to manage data streams.
Propose a CGRA architecture for stream applications based on the above model.
The RC is a cluster of multipliers and ALUs.
Decomposition and combination of RCs can be supported for flexibility of configurations.
The proposed CGRA is evaluated by the machine learning.
Average speedup and energy reduction is 39x and 1443x respectively comparing to CPU implementations.

## Slide 30
Thank you!

## Slide 31
Observations from object detection/classification domain:
Classical feature extraction algorithms: HOG
-1
0
1
-1
0
1
Compute gradients
cell
Accumulate weighted votes for gradient orientation over spatial cells
Feature map
Normalize contrasts within overlapping blocks of cells
Two overlapping blocks
Feature vector
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
The whole algorithm
This abstraction can be applied to Dense-SIFT, DPM algorithms
Appendix (1)
Stage 1
Stage 2
Stage 3

## Slide 32
Convolution in CNN: one of the computing strategies
#Phase 0
#Phase 1
Kernel size: ; stride: 2.
Appendix (2)