## Slide 1: Connect On the Fly: Enhancing and Prototyping of Cycle-Reconfigurable Modules
Hao Zhou∗, Xinyu Niu†, Junqi Yuan∗, Lingli Wang∗, Wayne Luk†
†Dept. of Computing, Imperial College London, UK
∗School of Microelectronics, Fudan University, China

## Slide 2: Outline
motivation
EURECA architecture
Architecture optimisation
results
summary

## Slide 3: Summary of Contributions
1. Reconfiguration strategies for data access patterns
  Three categories for dynamic data accesses
  Reconfiguration modes: maximise configuration sharing
2. Architecture design space exploration
  Multiplexers or permutation network
  Optimal EURECA module size
3. Prototype chip layout
  Manually developed with SMIC 130-nm technology
  Results measured using Cadence tools

## Slide 4: Static vs dynamic data access
conditional arithmetic operators
dynamic data access patterns
for (i=0; i<n; i+=N)
#parallel unroll N
for(j=0; j<N; j++){
k = i*N + j;
d[k] = a[k+1] * c[k];
}
for (i=0; i<n; i+=N)
#parallel unroll N
for(j=0; j<N; j++){
k = i*N + j;
d[k] = a[b[k+1]] * c[k];
}
static: easy
dynamic: hard
Notes: Static operations with deep pipeline suitable for FPGA, like the one on the left
Dynamic operations, which reply on runtime values to decide which operation to run, are hard to support in FPGAs, like the one on the right

## Slide 5: Example: dynamic data access
C
for (i=0; i<n; i++) {
d[k] = a[b[k+1]] * c[k];
}
d
connections for
one data-path: easy

## Slide 6: Example: dynamic data access
for (i=0; i<n; i+=N)
#parallel unroll N=32
for(j=0; j<32; j++){
k = i*32 + j;
d[k] = a[b[k+1]] * c[k];
}
connections for
32 data-paths: hard

## Slide 7: Implementation 1: multiplexors
d
congested routing
  1024-to-1024 bit connections
  unroutable in XC6V-SX475T
expensive user multiplexers
32 output ports, each 32-bit wide

## Slide 8: EURECA module: execution flow
Initial configuration
Initial configuration
CDN: Configuration Distribution Network
Notes: EURECA architectures take a different way: at each cycle, we only implement what’s needed
Circuits are configured cycle by cycle

## Slide 9: EURECA module: execution flow
Initial Connections
CG
Data-paths
CG: Configuration Generator

## Slide 10: Run-time reconfiguration flow
Initial Connections
CG
Runtime configuration

## Slide 11: Run-time reconfiguration flow
Initial configuration
CG

## Slide 12: Run-time reconfiguration flow
Initial configuration
CG
data-path data
memory data

## Slide 13: 1. Optimising Data Access Patterns
Static (a): accesses with fixed strides
Dynamic size (b): linear accesses with variable vector size
Dynamic offset (c): vector access with dynamic offsets
Random (d): each access with a dynamic offset
Notes: In this work, we put data access into 4 categories
The dynamic accesses have three patterns:
Each vector access has different data size (in figure, 3 bytes in cycle 1, 2 byes in cycle 2)
Each vector access has different starting point (in figure cycle1 starts from the 6th byte, cycle2 starts from the 2nd byte)
Each scalar access has random access location

## Slide 14: Dynamic FIFOs
Dynamic size  Dynamic FIFOs: BRAMs organised as FIFOs
  A single configuration is shared by all runtime reconfigurable connections in a EURECA module
  Enable signals to FIFOs are dynamically connected to corresponding FIFO ports
Notes: As data are always accessed in order (3,4,5,6,7,8….), we use FIFOs here
FIFOs are connected with EURECA modules
In this example, 3, 4, 5 need to be committed from the FIFO, access start from the 3rd memory port (3)
After the commitment, the data appear at the FIFO output ports are 9, 6, 7, 8
Access needs to start from the 2nd memory port (6)
Runtime reconfiguration is needed
To share configuration, we can order the connections in the way such that under the same configuration, the memory ports are connected in order:
For example, when configuration sets each connection to select its first input.
The first connection (pink module) connects to 1st memory port
The second connection (pink module) connects to 2nd memory port
Therefore, the whole EUREC module only needs 1 runtime configuration
This significantly reduces the logic to generate runtime configurations

## Slide 15: Dynamic cache
Dynamic offset Dynamic cache: BRAMs as shared cache
  Single configuration shared by all runtime reconfigurable connections
  Input address to BRAMs are dynamically connected
Notes: Similar here, the only difference is that since vector data are not accessed in order, each memory port needs its address input instead of FIFO read enables
Configurations can be shared in the same way

## Slide 16: Dynamic shared cache
Random  Dynamic shared cache: access conflicts
  Access conflicts happen when 2 or more data-paths try to access the same port at the same time: the lower two data-paths in the figure
  Each reconfigurable connection has a separate configuration
  Conflicted ports (the lowest data-path) are disabled by scheduler
Notes: For random access, to avoid runtime conflicts, a scheduler is needed to disable invalid runtime reconfiguration
Configurations cannot be shared for this case, each memory port has its own runtime configuration

## Slide 17: 2. Optimising Connection Network
Multiplexers or permutation network?
Three parameters to evaluate:
  Number of pins to support runtime reconfiguration
  Silicon area to implement the network
  Logic required to generate runtime configurations for the network

## Slide 18: Connection Network
Multiplexers or permutation network?
Multiplexers are selected as configurations can be shared
  To reconfigure a permutation network within a single cycle takes an unacceptable amount of pins and configuration generation logic
Notes: Permutation network has less area usage since the connections are split into multiple layers
However, these multiple layers are much more complicated to configure, and the runtime configurations cannot be shared
End up with too many pins to input all runtime configurations in a single clock cycle, and a huge configuration generator

## Slide 19: Architecture Efficiency
Architecture efficiency is evaluated with the area saved by runtime reconfiguration, multiplied by overall area overhead
Original chip area
Original application resource usage
Runtime reconfigurable application resource usage
EURECA chip area

## Slide 20: EURECA Optimisation
Connection network: multiplexers or permutation network
  Memory group size: the number of BRAM blocks connected to a single EURECA module
  Circuit models for application area reduction and module area
    Small memory group size: small reductions in design area
    Large memory group size: large module area overhead
  Efficiency reaches maximum at 32 BRAMs, supported by circuit models

## Slide 21: 3. EURECA Prototype
Prototype layout developed with SMIC 130-nm technology
  Classic island-style FPGA architecture adapted
  Small FPGA size due to tape-out budget
  A single EURECA module added to one column of BRAMs (8)
Prototype layout developed with SMIC 130-nm technology
  A EURECA module is the same area as 2.72 CLB columns
  A EURECA module brings 1.15ns delay (typical circuit critical path delay on this architecture 20-40 ns)

## Slide 22: EURECA Prototype

## Slide 23: Application 1: Large-scale Sorting
Large-scale sorting: dynamic FIFOs
  At each cycle, there are unknown amount of values committed from each FIFO
  The starting address changes from cycle to cycle
Notes: Large-scale sorting, is one of the most extensively researched subjects because of the need to quickly organise millions to billions data items in a database.

## Slide 24: Application 2: Memcached
Memcached: dynamic cache
  A vector data pointed by a dynamic pointer is read each cycle
  The address changes from cycle to cycle
Notes: Memcached, is a distributed memory caching system widely used in the servers of web service companies (Facebook, Twitter, YouTube, Wikipedia, etc.). A Memcached server stores frequently ac- cessed data in memory to provide quick responses to web requests.

## Slide 25: Application 3: SpMV
SpMV: dynamic shared cache
  Accessed locations in the vector depends on the postion of non-zeros in the sparse matrix
  Each vector access is random
  A scheduler module to only enable one runtime reconfiguration for a memory port
Notes: Sparse Matrix-Vector multiplication (SpMV), is widely used in scientific computing and industrial development. SpMV multiplies a sparse matrix with a dense vector,

## Slide 26: Experimental Setup
Target chip
  Prototype EURECA chip
  Area, delay measured from Cadence simulation results
synthesis environment
  Design Compiler (DC) for circuit synthesis
  ABC for mapping
  A graph matching algorithm for packing
  Simulated annealing algorithm for placement
  Path-finder for routing

## Slide 27: Application Performance
Three implementations developed for each application
  Static design use LUTs to support all dynamic data accesses
  EURECA supports dynamic accesses with original architecture
  Dynamic uses the optimised architecture, support maximum configuration sharing

## Slide 28: Application Performance
Three implementations developed for each application
  Up to 11.2 times area-delay reductions compared with static design
  Up to 1.39 times area-delay reduction compared with original EURECA architecture

## Slide 29: Application Performance
Area-delay reductions grows linearly as the number of BRAMs connected to a EURECA module grows
  Area reduction increases to 16 for 32 BRAMs

## Slide 30: Current and future work
EURECA full-stack compiler
EURECA programming models
  operation mapping
  data access mapping
  many-region communication
EURECA simulator for architecture optimisation
  Automatically explore design space with generated architecture files and Verilog modules

## Slide 31: Summary: EURECA
Routing challenge: dynamic data access applications
  Three data access patterns
  Optimised reconfiguration strategies
  Design space exploration and prototype layout
Experimental results: prototype layout + synthesis tool
  small area and delay overhead
Application performance
  up to 1/11.2x area-delay product compared with static architecture
  up to 1/1.39x area-delay product compared with initial architecture